## Slide 1: Turbulence Modelling for Smoothed Particle Hydrodynamics K T Prajwal Prathiksh
Supervisor: Prof. Prabhu Ramachandran
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022
Dual Degree Project (Stage I) - Presentation
Notes: Buy Aeroelasticity (Dover Books on Aeronautical Engineering) Book Online at Low Prices in India | Aeroelasticity (Dover Books on Aeronautical Engineering) Reviews & Ratings
Merging Radius between two vortices
Summarize the russian paper
Sine wave/Saw tooth wave/Squre wave - heaving motion for the cylinder

## Slide 2: Introduction
Lagrangian Modelling – SPH
  No background mesh
  Handles large deformations, complex boundary dynamics
  Simplified model implementation
  Highly & efficiently parallelizable
Turbulent Flow
  Characterization
      High Reynolds number flows
      Random spatial & temporal velocity fluctuations
      Rotational & 3D velocity field
      Large mixing capacity of the flow
      Chaotic nature of solutions
  Modelling
      Lacks analytical solutions except for simple cases
      CFD simulations required for complex flows
      Typical modelling techniques
          Governing equations  Averaged or filtered
          Closure problem  Fluctuating components modelled using mean flow properties
          Stochastic methods
      Models mostly based on Eulerian framework

## Slide 3: Project Objectives
Turbulence Modelling in SPH
  Lacks robust & accurate models
  Shortcomings of current models:
    Cannot be generalized to various types of turbulence-based problems
    Issues in scaling to 3D turbulent flows
      Accuracy & computational constraints
    Boundary conditions & treatment not well established
Project Objective
  Review state of the art turbulence models in SPH
  Provide advantages & disadvantages of the major categories of models
  Extend promising models to robust & accurate SPH schemes[1]
  Analyze & study its performance in bounded turbulent flow
  Improve overall scheme using recent developments of SPH
[1] P. Negi and P. Ramachandran, “How to train your solver: A method of manufactured solutions for weakly compressible smoothed particle hydrodynamics,” Phys. Fluids, vol. 33, no. 12, 2021, doi: 10.1063/5.0072383.
Existing
Models
Expected
Outcome

## Slide 4
Turbulence Modelling
Project’s Progress
Surveyed research papers detailing work on turbulence models for SPH (c. 2000 – 2022)
Classified 5 major categories of turbulence models
Identified a systematic, model-evaluation method
    Benchmark problems feasible with SPH
    Post-simulation analysis techniques
Turbulence Models
Viscosity
LES
Lagrangian-LES
RANS
LANS
Artificial
Stochastic
Implicit P-Poisson
Explicit P-EOS

## Slide 5: Turbulence Modelling
Surveyed research papers detailing work on turbulence models for SPH (c. 2000 – 2022)
Classified 5 major categories of turbulence models
  [chart]
Identified a systematic, model-evaluation method
  Benchmark problems amenable to SPH
  Post-simulation analysis techniques

## Slide 6: Viscosity-based Models
Eddy Viscosity Model [Violeau]
  One of the first classes of SPH turbulence models
  Velocities are Reynolds-averaged
  First-order closure model  Reynolds stress tensor & mean vel gradients
  Considered the turbulent eddy viscosity
  Simulated Poiseuille flow
    Reproduced log-law profile near walls
    Appropriate for shear flows
GLM [Violeau]
  Prescribed the particle velocity as a random process
  Same test-case as earlier considered
  Large deviations observed
  Can be generalized to various flows unlike earlier model
  Images?
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 7: Viscosity-based Models
mSPH [Adami2012]
  Observed absence of viscosity  Noisy particle motion
  Finite viscosity  Over-predict dissipation
  Modified EOS & momentum eq to homogenise particle distribution (to stabilise scheme)
  Simulated 2D Taylor-Green Vortex (TGV)
    Observed merging of vortices [Q]
    Energy cascade (Kolmogorv scale) slopes: mSPH (-3), standard SPH (1)
  Simulated 3D Taylor-Green Vortex (TGV)
    Can simulate transitional flow with reasonable dissipation rate
  mSPH similar to eddy viscosity model below numerical resolution
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 8: Large-Eddy Simulation-based Models
Implicit Pressure Poisson-based Models
  [Gotoh2004, 2005] Considered incompressible flow
  Filtered the Navier-Stokes (NS) eqs (Spatial filter)
  Stress Tensor  Closed using Boussinesq’s Hypothesis
  Eddy viscosity  Estimated using Smagorinsky Model
    Model is modified to incl wall effects, s.t., it is not over-dissipative inside laminar layer
  System evolved using the predictive-corrective time integrator
    Requires the implicit solution of the pressure poisson equation
  Simulated:
    2D wave interaction with partially immersed breakwater
    2D wave breaking on a beach
    Accurately tracked free surfaces with large deformation
    Surfaces did not exhibit numerical diffusion
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 9: Large-Eddy Simulation-based Models
Explicit Pressure Poisson-based Models
  [Rogers2005] Considered compressible flow
  Averaged the NS eqs (Favre averaging)
  Filtered the Navier-Stokes (NS) eqs (Spatial filter)
  Observed density variations in compressible SPH  Unphysical behaviour on free surfaces
    Performed Shepard filtering of density every 40 time steps
  Simulated:
    Weakly plunging breaker in 2D & 3D
    2D green-water overtopping, 2D & 3D wave breaking, 3D dam break [Rogers2006]
    Model predicted regions of high vorticity in 2D
    Model captured vertically oriented eddies in 3D
    Accurate for flow separation or splash-based problems
    Requires large number of particles, and very small time steps
    Uncertain regarding scalability to large-scale problems
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 10: Large-Eddy Simulation-based Models
Explicit Pressure Poisson-based Models
  [Canelas2016] Observed the standard Smagorinsky model cannot enforce wall conditions and non-vanishing stresses with laminar flows.
  Wall-adapting local eddy viscosity (WALE) model
  Simulated:
    Array of cylinders in 2D flow
    Studied LCS of the flow
    Observed recombination of vortices to larger structures
    Vortices with opposing strengths cancelled each other
    Believe such interactions lead to difficulty in interpreting the energy spectrum
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 11: Large-Eddy Simulation-based Models
Explicit Weakly Compressible Models
  [Okraschevski2022] Reinterpret SPH as a Lagrangian quadrature technique for explicit LES eqs
    Kernel scale limits SPH’s physical resolution  Unsuitable DNS alternative
  Considered spatial filtering on compressible NS
  Compared multiple Smagorinsky models (standard, sigma, MCG-form)
  Simulated 3D TGV
    All of the Smagorisnky models reduced the averaged kinetic energy
    Did not predict the dissipation rates accurately
  Overall comments:
    [fig2.14a,c]
    SPH can capture turbulence up to kernel scale at a high cost
    Explicit SFS models will remove kinetic energy, heightening the energy deficit of standard SPH
    Such models in an SPH framework can only degrade the quality of the approximation for subsonic turbulent flow [rennehan2021mixing]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 12: Lagrangian LES-based Models
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 13: RANS-based Models
[Shao2006, Wang2020]
  Considered incompressible, unsteady RANS equations
  Evolved using predictor-corrector scheme  Implicit pressure poisson equation
  Coefficients of the transport equations are empirically defined
  Simulated:
    2D wave breaking and overtopping of sloping wall [Shao2006]
    2D solitary wave propagating over a bottom-mounted barrier [Wang2020]
  Comments:
    coefficients derived from a quasi-steady state may behave sub-optimally in transient flow
    model would require further sensitivity analysis for the turbulence model and spatial resolution for improved results, despite being reasonably accurate in tracking free surfaces.
    Underpredicts max k, sensitive to initial seeding of k
    Effects of physical viscous dissipation and numerical dissipation needs to be balanced aptly
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 14: LANS-based Models
[holm1998euler, Marsden2001] Lagrangian averaged NS equations (LANS-) considered
  Averaging technique employed at the level of the variational principle from which NS eqs are derived
  denotes scale of rapid fluctuations in the flow map
[Monaghan2002] Formulated the SPH- model based on the LANS- eqs
  Considered smoothed velocity for particle transport
  Momentum eq had to solved iteratively
[Monaghan2011, Monaghan2017] Derived the SPH- model
  Explicit momentum equation with a viscous term
  Simulated 2D flow past a cylinder moving along a Lissajous curve
  predict satisfactory results for the velocity correlation functions, energy spectrum and mixing while having particle resolution be half of that required for a DNS with a resolution the Reynolds length
  higher Reynolds numbers and other boundary conditions, such as free surfaces, will need to be studied further
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 15: Miscellaneous Models
[Liu2019] Devised a viscosity-based vorticity correction technique
  Aimed primarily towards benefiting the CGI community
  Work focuses more on visual artifacts of the flow, not quantified metrics
  Builds on the fact that rotational kinetic energy translational kinetic energy
[Obeidat2018] Devised a hybrid-SPH scheme
  Employs Eulerian mesh to evaluate the governing equations
  Values interpolated to particles which advect
  Remeshing is performed when particle distribution is not uniform
  Information from the model cannot help improve traditional SPH schemes
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 16: Evaluation of Turbulence Models
Most of Lagrangian turbulent models seem to be tested for only complex surface flows
Systematic analysis of isotropic turbulence problems provides greater insight into the energy spectrum and its corresponding cascade across varying length scales.
Appropriate bounded/periodic test cases must be used when analyzing turbulence
Energy cascade might not always be apt? Use coherent structures, vorticity, other suitable metrics [Q]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 17: Benchmark Problems
Taylor-Green Vortex Problem
  2D Case
    Periodic, incompressible flow
    Analytical solutions known
  3D Case
    Initial flow conditions can be specified
Thin Double-Shear Layer
  Flow under-resolved  Spurious structures are produced
  Generation of the spurious structure depends on the scheme
3D Isotropic Turbulence
  DNS dataset from the JHU Turbulence database Cluster [li2008public]
  Dataset: Incompressible flow with isotropic and forced turbulence.
  - Spatial points, with time samples spanning one large-scale turnover time
2D Confined & Driven Turbulence
  2D fluid confined to a square box enclosing a cylinder
  Cylinder moves in a predetermined trajectory
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 18: Post-Simulation Analysis
Energy spectral density
  Velocity field over a grid generated using suitable interpolation of the particle velocity data [Shi2013]
  Fourier transform of the velocity field performed  Velocity spectrum as a function of the wave-number
  Energy spectrum computed from the velocity spectrum
Velocity gradient-based metrics
  SPH formulations exist
  some situations, most of the definitions of the vortex are not objective and suitable for studying the flow, particularly in the context of $3D$ flow. [haller2005]
Lagrangian coherent structures
  Local velocity fluctuations do not induce noise
  FTLE is formulated in the Lagrangian framework  Better identification of LCSs
  SPH formulations available [sun2016]
  Analysis flexibility:
    backward-in-time FTLE can be computed using limited resources during run-time concurrently in this method. However, the forward-in-time FTLE can only be computed during post-processing.
    Easily parallelizable
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 19: Conclusion & Future Work
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 20
Thank you!
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022

## Slide 21: Blank Template Slides

## Slide 22
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 24: Filled Template Slides

## Slide 25: Project Motivation
Motion of Biological Swimmers
Study of Forces
Study of Energetics
High-Fidelity - CFD Solvers
Simulation Parameters
Reynolds number
Swimming trajectories
Single/Multi Swimmers
Placements & Configurations
Boundary Conditions
Geometry
And many more...
Develop underwater vehicles with:
better mobility
lower noise
higher endurance
efficiency
Low-Fidelity - Theoretical or Computational Frameworks
Project Outcome
Gain better understanding of the problem at hand
Utilizes lesser resources
Allows for faster iteration over models

## Slide 26: Conclusion
Thrust produced continuously → Output is not stable.
Sharp peaks in thrust production coincide with vortex shedding.
Airfoil starts its heaving motion with downwards stroke → Small negative lift is produced (average)
Airfoil starts its heaving motion with upwards stroke → Small positive lift is produced (average).
General trend in bulk movement of shed vortices as shown by Dynnikova[1] is observed.
Fig: Vortex wakes behind an airfoil performing angular oscillations[7]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.