## Slide 1: Turbulence Modelling for Smoothed Particle Hydrodynamics K T Prajwal Prathiksh
Supervisor: Prof. Prabhu Ramachandran
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022
Dual Degree Project (Stage I) - Presentation
Notes: Buy Aeroelasticity (Dover Books on Aeronautical Engineering) Book Online at Low Prices in India | Aeroelasticity (Dover Books on Aeronautical Engineering) Reviews & Ratings
Merging Radius between two vortices
Summarize the russian paper
Sine wave/Saw tooth wave/Squre wave - heaving motion for the cylinder

## Slide 2: Introduction
Lagrangian Modelling – SPH
  No background mesh
  Handles large deformations, complex boundary dynamics
  Simplified model implementation
  Highly & efficiently parallelizable
Turbulent Flow
  Characterization
      High Reynolds number flows
      Random spatial & temporal velocity fluctuations
      Rotational & 3D velocity field
      Large mixing capacity of the flow
      Chaotic nature of solutions
  Modelling
      Lacks analytical solutions except for simple cases
      CFD simulations required for complex flows
      Typical modelling techniques
          Governing equations  Averaged or filtered
          Closure problem  Fluctuating components modelled using mean flow properties
          Stochastic methods
      Models mostly based on Eulerian framework

## Slide 3: Project Objectives
Turbulence Modelling in SPH
  Lacks robust & accurate models
  Shortcomings of current models:
    Cannot be generalized to various types of turbulence-based problems
    Issues in scaling to 3D turbulent flows
      Accuracy & computational constraints
    Boundary conditions & treatment not well established
Project Objective
  Review state of the art turbulence models in SPH
  Provide advantages & disadvantages of the major categories of models
  Extend promising models to robust & accurate SPH schemes[1]
  Analyze & study its performance in bounded turbulent flow
  Improve overall scheme using recent developments of SPH
[1] P. Negi and P. Ramachandran, “How to train your solver: A method of manufactured solutions for weakly compressible smoothed particle hydrodynamics,” Phys. Fluids, vol. 33, no. 12, 2021, doi: 10.1063/5.0072383.
Existing
Models
Expected
Outcome

## Slide 4
Turbulence Modelling
Project’s Progress
Surveyed research papers detailing work on turbulence models for SPH (c. 2000 – 2022)
Classified 5 major categories of turbulence models
Identified a systematic, model-evaluation method
    Benchmark problems feasible with SPH
    Post-simulation analysis techniques
Turbulence Models
Viscosity
LES
Lagrangian-LES
RANS
LANS
Artificial
Stochastic
Implicit P-Poisson
Explicit P-EOS

## Slide 5: Viscosity-based Models
Eddy Viscosity Model[1]
  One of the first classes of SPH turbulence models
  Velocities are Reynolds-averaged
  First-order closure model:
    Reynolds stress tensor & mean velocity gradients
  Turbulent eddy viscosity considered
  Simulated Poiseuille flow
  Comments
    Reproduced log-law profile near walls
    Appropriate for shear flows
[1] D. VIOLEAU, S. PICCON, and J.-P. CHABARD, “TWO ATTEMPTS OF TURBULENCE MODELLING IN SMOOTHED PARTICLE HYDRODYNAMICS,” in Advances in Fluid Modeling and Turbulence Measurements, Jul. 2002, vol. 1, no. 5, pp. 339–346, doi: 10.1142/9789812777591_0041.
Fig: Computed mean velocity profile of turbulent Poiseuille flow in a pipe (Rep: Violeau et al)

## Slide 6: Viscosity-based Models
Generalized Langevin Model[1]
  Prescribed the particle velocity as a random process
  Acceleration  Function of a random vector (non-correlated with velocity)
  Simulated Poiseuille flow
  Comments
    Mean operator appeared to behave like a LES filter
    Large deviations observed in mean velocity profile
    Can be generalized to various types of turbulent flows, & not only shear flows
[1] D. VIOLEAU, S. PICCON, and J.-P. CHABARD, “TWO ATTEMPTS OF TURBULENCE MODELLING IN SMOOTHED PARTICLE HYDRODYNAMICS,” in Advances in Fluid Modeling and Turbulence Measurements, Jul. 2002, vol. 1, no. 5, pp. 339–346, doi: 10.1142/9789812777591_0041.
Fig: Computed mean velocity profile of turbulent Poiseuille flow in a pipe (Rep: Violeau et al)

## Slide 7: Viscosity-based Models
Modified-SPH (mSPH)[1]
  Observation: Absence of viscosity  Noisy particle motion
  Finite viscosity  Over-prediction of dissipation
  Modified EOS & MOM eqs.  Particle distribution homogenised
  Simulated:
    2D Taylor-Green Vortex (TGV)
    3D Taylor-Green Vortex (TGV)
  Comments
    Merging of vortices observed
    Energy cascade (Kolmogorv scale) slopes reproduced
      mSPH (-3); standard SPH (1)
    Transitional flow simulated with reasonable dissipation rate
    mSPH Eddy viscosity model below numerical resolution
[1] S. Adami, X. Y. Hu, and N. A. Adams, “Simulating three-dimensional turbulence with SPH,” 2012.
Fig: Velocity vector plot at t=2 (left) and t=30 (right). (Rep: Adami et al)

## Slide 8: Large-Eddy Simulation-based Models
Implicit Pressure Poisson-based Models[1,2]
  Assumption: Incompressible flow
  Navier-Stokes (NS) eqs.  Spatially filtered
  Stress tensor  Closed using Boussinesq’s hypothesis
  Eddy viscosity  Estimated using modified Smagorinsky model
    Model modified to include wall effects
  Predictive-corrective time integrator
    Requires implicit solution of pressure poisson eq
  Simulated:
    2D wave interaction with partially immersed breakwater[1]
    2D wave breaking on a beach[2]
  Comments
    Accurately tracked free surfaces with large deformation
    Surfaces did not exhibit numerical diffusion
    Scheme’s accuracy:
[1] H. Gotoh, S. Shao, and T. Memita, “SPH-LES model for numerical investigation of wave interaction with partially immersed breakwater,” Coast. Eng. J., vol. 46, no. 1, pp. 39–63, 2004, doi: 10.1142/S0578563404000872.
[2] S. Shao and H. Gotoh, “Turbulence particle models for tracking free surfaces,” J. Hydraul. Res., vol. 43, no. 3, pp. 276–289, May 2005, doi: 10.1080/00221680509500122.
Fig: Time sequences of wave profile. (Rep: Gotoh et al)
Notes: Model is modified to include wall effects, s.t., it is not over-dissipative inside laminar layer

## Slide 9: Large-Eddy Simulation-based Models
Explicit Pressure EOS-based Models[1,2]
  Assumption: Compressible flow
  NS eqs  Favre averaged
  Observation: Density variations  Unphysical behaviour on free surfaces
    Shepard filtering of density performed periodically
  Simulated:
    Weakly plunging breaker in 2D & 3D[1]
    2D green-water overtopping, 2D & 3D wave breaking, 3D dam break[2]
  Comments
    Model predicted regions of high vorticity in 2D
    Model captured vertically oriented eddies in 3D
    Accurate for flow separation or splash-based problems
    Requires large & very small
    Uncertain regarding scalability to large-scale problems
[1] B. D. ROGERS and R. A. DALRYMPLE, “SPH MODELING OF BREAKING WAVES,” in Coastal Engineering 2004, Apr. 2005, pp. 415–427, doi: 10.1142/9789812701916_0032.
[2] R. A. Dalrymple and B. D. Rogers, “Numerical modeling of water waves with the SPH method,” vol. 53, pp. 141–147, 2006, doi: 10.1016/j.coastaleng.2005.10.004.

## Slide 10: Large-Eddy Simulation-based Models
Explicit Pressure EOS-based Models[1]
  Observation: Standard Smagorinsky model cannot enforce
    Wall conditions
    Non-vanishing stresses with laminar flows
  Devised Wall-adapting local eddy viscosity model (WALE)
  Simulated an array of cylinders in 2D flow
  Comments
    LCS captured reasonably well
    Observed merging of vortices to larger structures
    Interactions of vortices with opposing strengths  Vorticity cancellation
    Claim: Complex vortex interactions  Possible difficulty in interpreting the energy spectrum
[1] R. B. Canelas, A. M. Ricardo, R. M. L. Ferreira, J. M. Domínguez, and A. J. C. Crespo, “Hunting for Lagrangian Coherent Structures : SPH-LES turbulence simulations with Wall-adapting Local Eddy Viscosity ( WALE ) model,” 11th SPHERIC, no. March 2017, 2016, [Online].
Fig: Backward-in-time FTLE field. (Rep: Canelas et al)

## Slide 11: Large-Eddy Simulation-based Models
Explicit Pressure EOS-based Models[1]
  Reinterpret SPH  Lagrangian quadrature technique for explicit LES
    Kernel scale limits SPH’s physical resolution  Unsuitable DNS alternative
  Navier-Stokes (NS) eqs.  Spatially filtered
  Compared multiple Smagorinsky models
    (standard, , MCG-form)
  Simulated 3D TGV
  Comments
    Smagorisnky models reduced averaged kinetic energy
    Dissipation rates not predicted accurately
    SPH can capture turbulence up to kernel scale (high cost)
    Explicit SGS models remove kinetic energy  Increases energy deficit of standard SPH
    “SGS models in SPH framework only degrade the quality of the subsonic turbulent flow approximation”[2]
[1] M. Okraschevski, N. Bürkle, R. Koch, and H.-J. Bauer, “Smoothed Particle Hydrodynamics Physically Reconsidered -- The Relation to Explicit Large Eddy Simulation and the Issue of Particle Duality,” 2022, [Online].
[2] D. Rennehan, “Mixing matters,” Mon. Not. R. Astron. Soc., vol. 506, no. 2, pp. 2836–2852, 2021.
Fig: Density-weighted averaged kinetic energy (top), averaged dissipation rate (bottom). (Rep: Okraschevski et al)

## Slide 12: Lagrangian LES-based Models
Lagrangian form of LES[1,2]
  Assumption: Weakly compressible flow
  Lagrangian filter - (compact support, even) introduced
  decomposed into independent spatial & temporal components
  Governing eqs. written using spatially filtered terms
    Temporal terms of higher order neglected
    Continuity eq. closed using Fick-like diffusion term
    MOM eq. closed using Yoshizawa-model for the stress tensor
    Considered -SPH formulation
  Simulated:
    2D TGV
    3D homogenous turbulence
  Comments
    The model overcomes issues of spurious high-frequency noise & onset of tensile instability (High flows)
    The energy spectra agrees well with theoretical decay rate
    Wall functions need to be incorporated to deal with boundaries
    Higher-order approach can significantly improve the performance
[1] A. Di Mascio, M. Antuono, A. Colagrossi, and S. Marrone, “Smoothed particle hydrodynamics method from a large eddy simulation perspective,” Phys. Fluids, vol. 29, no. 3, 2017, doi: 10.1063/1.4978274.
[2] A. Colagrossi, “Smoothed particle hydrodynamics method from a large eddy simulation perspective . Generalization to a quasi-Lagrangian model Smoothed particle hydrodynamics method from a large eddy simulation perspective . Generalization to a quasi-Lagrangian model,” vol. 015102, no. December 2020, 2021, doi: 10.1063/5.0034568.
Fig: Energy spectrum (left), field (right). (Rep: Colagrossi2021)

## Slide 13: RANS-based Models
Models[1,2]
  Considered incompressible, unsteady RANS equations
  Predictive-corrective time integrator
    Requires implicit solution of pressure poisson eq
  Simulated:
    2D wave breaking and overtopping of sloping wall[1]
    2D solitary wave propagating over a bottom-mounted barrier[2]
  Comments
    Accurately tracks free-surfaces
    coefficients (empirically derived from quasi-steady state) perform sub-optimally in transient flow
    Model requires a sensitivity analysis for the turbulence model & spatial resolution for improved performance
    Underpredicts max & is sensitive to initial seeding of
    Effects of viscous dissipation & numerical dissipation need to be balanced
[1] S. Shao, “Incompressible SPH simulation of wave breaking and overtopping with turbulence modelling,” no. May 2005, pp. 597–621, 2006.
[2] D. Wang and P. L. F. Liu, “An ISPH with k–ε closure for simulating turbulence under solitary waves,” Coast. Eng., vol. 157, no. July 2019, p. 103657, 2020, doi: 10.1016/j.coastaleng.2020.103657.
Fig: Water surface elevations. (Rep: Shao et al)c

## Slide 14: LANS-based Models
Lagrangian-averaged NS eqs. (LANS-) Models[1,2,3,4]
  Lagrangian-averaging[1]: Performed at the level of variational principle from which NS eqs. are derived
    denotes scale of rapid fluctuations in the flow map
  SPH- model[2]  Initial models based on LANS- eqs.
    Particle transport  Smoothed velocity
    MOM eq. solved iteratively
  SPH- model[3,4]  Improvement of SPH- model
    Explicit MOM eq. with viscous term
  Simulated 2D flow past a cylinder moving along a Lissajous curve[4]
  Comments
    Bounded (no-slip) flow implies is neither periodic/isotropic  Author prefers correlation functions over energy spectrum
    Satisfactory results for velocity correlation functions, energy spectrum & mixing with half the particle resolution of DNS
    Flows with larger Reynolds numbers & other boundary conditions, such as free surfaces need to be studied
[1] J. E. Marsden and S. Shkoller, “Global well-posedness for the Lagrangian averaged Navier-Stokes (LANS-α) equations on bounded domains,” Philos. Trans. R. Soc. A Math. Phys. Eng. Sci., vol. 359, no. 1784, pp. 1449–1468, 2001, doi: 10.1098/rsta.2001.0852.
[2] J. J. Monaghan, “SPH compressible turbulence,” vol. 852, pp. 843–852, Apr. 2002, doi: 10.1046/j.1365-8711.2002.05678.x.
[3] J. J. Monaghan, “A turbulence model for smoothed particle hydrodynamics,” Eur. J. Mech. B/Fluids, vol. 30, no. 4, pp. 360–370, 2011, doi: 10.1016/j.euromechflu.2011.04.002.
[4] J. J. Monaghan, “SPH-ϵ simulation of 2D turbulence driven by a moving cylinder,” Eur. J. Mech. B/Fluids, vol. 65, pp. 486–493, 2017, doi: 10.1016/j.euromechflu.2017.03.011.
Fig: Stirring of coloured particles. (Rep: Monaghan2017)

## Slide 15: Miscellaneous Models
Viscosity-based vorticity correction model[1]
  Aimed primarily towards benefiting the CGI community
    Faster computational time & simplified system of equations
  Research focuses more on visual artifacts of the flow, not quantified metrics
  Builds on the fact that rotational kinetic energy translational kinetic energy
Hybrid-SPH (hrSPH)[2]
  Particle data interpolated onto Eulerian mesh grids
  Rate of change of flow properties computed on mesh grid
  Updated mesh values interpolated onto particles
  Advection of particles using the updated properties
  Remeshing is performed when particles cluster to ensure uniform particle distribution
  Information from the model cannot help improve traditional SPH schemes
[1] S. Liu, X. Wang, X. Ban, Y. Xu, J. Zhou, and Y. Zhang, “Viscosity-based Vorticity Correction for Turbulent SPH Fluids,” in 2019 IEEE Conference on Virtual Reality and 3D User Interfaces (VR), Mar. 2019, pp. 1048–1049, doi: 10.1109/VR.2019.8798224.
[2] A. Obeidat and S. P. A. Bordas, “Three-dimensional remeshed smoothed particle hydrodynamics for the simulation of isotropic turbulence,” Int. J. Numer. Methods Fluids, vol. 86, no. 1, pp. 1–19, 2018, doi: 10.1002/fld.4405.

## Slide 16
Evaluation of Turbulence Models
Most of Lagrangian turbulent models  Tested for primarily complex, free-surface flows
A systematic analysis of isotropic turbulence problems provides better insight on the energy spectrum & its cascade across varying length scales
Appropriate bounded/periodic test cases must be used when analyzing turbulence
Analyse results with appropriate metrics, and validate the results with experimental or numerical data from literature
Benchmark Problems
Various Turbulence Models
Post-simulation Analysis
Model Validation
Model Improvement

## Slide 17: Benchmark Problems
Taylor-Green Vortex Problem  Periodic, incompressible flow
  2D Case: Analytical solutions known
  3D Case: Initial flow conditions can be specified
Thin Double-Shear Layer
  Flow under-resolved  Spurious structures are produced
  Generation of the spurious structure depends on the scheme
3D Isotropic Turbulence[1]
  DNS dataset from the JHU Turbulence database Cluster
  Dataset: Incompressible flow with isotropic and forced turbulence.
  spatial points & time samples spanning one large-scale turnover time
2D Confined & Driven Turbulence[2]
  2D fluid confined to a square box enclosing a cylinder
  Cylinder moves in a predetermined trajectory
[1] Y. Li et al., “A public turbulence database cluster and applications to study Lagrangian evolution of velocity increments in turbulence,” J. turbul., vol. 9, p. N31, 2008.
[2] J. J. Monaghan, “SPH-ϵ simulation of 2D turbulence driven by a moving cylinder,” Eur. J. Mech. B/Fluids, vol. 65, pp. 486–493, 2017, doi: 10.1016/j.euromechflu.2017.03.011.

## Slide 18: Post-Simulation Analysis
Energy spectral density
  Velocity field over a grid generated using suitable interpolation of the particle velocity data[1]
  Fourier transform of the velocity field  Velocity spectrum as a function of the wave-number
  Energy spectrum computed from the velocity spectrum
Velocity gradient-based metrics
  Iso-vorticity surfaces, Q-criterion, -criterion, etc.
  Most of the definitions for a vortex  Not objective & suitable for studying the flow (esp. 3D flow)[2]
Lagrangian coherent structures (LCS)
  Local velocity fluctuations do not induce noise in LCS
  FTLE is formulated in the Lagrangian framework  Better identification of LCSs
  Provides flexibility in its formulation[3]
    Backward-in-time FTLE can be computed using limited resources during run-time concurrently
    Forward-in-time FTLE can only be computed during post-processing
    Easily parallelizable
[1] Y. Shi, X. X. Zhu, M. Ellero, and N. A. Adams, “Analysis of interpolation schemes for the accurate estimation of energy spectrum in Lagrangian methods,” Comput. Fluids, vol. 82, pp. 122–131, 2013, doi: 10.1016/j.compfluid.2013.05.003.
[2] G. Haller, “An objective definition of a vortex,” J. Fluid Mech., vol. 525, pp. 1–26, 2005.
[3] P. N. Sun, A. Colagrossi, S. Marrone, and A. M. Zhang, “Detection of Lagrangian Coherent Structures in the SPH framework,” Comput. Methods Appl. Mech. Eng., vol. 305, pp. 849–868, 2016, doi: 10.1016/j.cma.2016.03.027.

## Slide 19: Conclusion & Future Work
Stage – I outcome:
  A reasonable compilation of past SPH turbulence models
  The corresponding advantages, limitations & potential areas for refinement are understood
Entropically Damped Artificial Compressibility (EDAC) scheme[1]  Explicit incompressible SPH method
  Uses a pressure evolution eq. instead of the continuity equation[2]
  Produces a smoother & accurate pressure distribution for flows, confined or free
  Does not require artificial viscosity
Turbulence Models for EDAC
  Incompatible with RANS due to incompressibility condition
    Will consider compressible EDAC scheme to devise a turbulence model
  Lagrangian LES filtering of the pressure eq  Mixed filtered term obtained; cannot be decoupled further
    Will investigate potential closure models to decouple/model the mixed term
[1] P. Ramachandran and K. Puri, “Entropically damped artificial compressibility for SPH,” Comput. Fluids, vol. 179, pp. 579–594, Jan. 2019, doi: 10.1016/j.compfluid.2018.11.023.
[2] J. R. Clausen, “Entropically damped form of artificial compressibility for explicit simulation of incompressible flow,” Phys. Rev. E - Stat. Nonlinear, Soft Matter Phys., vol. 87, no. 1, pp. 1–12, 2013, doi: 10.1103/PhysRevE.87.013309.

## Slide 20
Thank you!
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022