## Slide 1: Turbulence Modelling for Smoothed Particle Hydrodynamics K T Prajwal Prathiksh
Supervisor: Prof. Prabhu Ramachandran
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022
Dual Degree Project (Stage I) - Presentation
Notes: Buy Aeroelasticity (Dover Books on Aeronautical Engineering) Book Online at Low Prices in India | Aeroelasticity (Dover Books on Aeronautical Engineering) Reviews & Ratings
Merging Radius between two vortices
Summarize the russian paper
Sine wave/Saw tooth wave/Squre wave - heaving motion for the cylinder

## Slide 2: Introduction
Turbulent Flow:
  Characterization:
    High Reynolds number flows
    Random spatial & temporal velocity fluctuations
    Rotational & 3D velocity field
    Large mixing capacity of the flow
    Chaotic nature of the solutions
  Modelling:
    Lack analytical solutions except for simple flow cases
    CFD simulations required for complex flow cases
    Typical modelling techniques
      Governing equations  Averaged or filtered
      Closure problem  Model fluctuating components using mean flow properties
      Stochastic methods
    Eulerian frameworks
Lagrangian Modelling – SPH:
  No background mesh required  Large deformations, complex boundary dynamics
  Simplifies model implementation and parallelization to multi-core architectures

## Slide 3: Project Objectives
Turbulence Modelling in SPH
  Lacks robust models
  Shortcomings of current models –
    Cannot be generalized to various turbulence-based problems
    Issues in scaling to 3D flows
Project Objective
  Review state of the art turbulence models in SPH
  Provide advantages & disadvantages of the major classes of models
  Extend promising models to robust & accurate SPH schemes [negi]
  Analyze & study its performance in bounded turbulent flows

## Slide 4: Turbulence Modelling
Surveyed research papers detailing work on turbulence models for SPH (c. 2000 – 2022)
Classified 5 major categories of turbulence models
  [chart]
Identified a systematic, model-evaluation method
  Benchmark problems amenable to SPH
  Post-simulation analysis techniques

## Slide 5: Viscosity-based Models
Eddy Viscosity Model [Violeau]
  One of the first classes of SPH turbulence models
  Velocities are Reynolds-averaged
  First-order closure model  Reynolds stress tensor & mean vel gradients
  Considered the turbulent eddy viscosity
  Simulated Poiseuille flow
    Reproduced log-law profile near walls
    Appropriate for shear flows
GLM [Violeau]
  Prescribed the particle velocity as a random process
  Same test-case as earlier considered
  Large deviations observed
  Can be generalized to various flows unlike earlier model
  Images?
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 6: Viscosity-based Models
mSPH [Adami2012]
  Observed absence of viscosity  Noisy particle motion
  Finite viscosity  Over-predict dissipation
  Modified EOS & momentum eq to homogenise particle distribution (to stabilise scheme)
  Simulated 2D Taylor-Green Vortex (TGV)
    Observed merging of vortices [Q]
    Energy cascade (Kolmogorv scale) slopes: mSPH (-3), standard SPH (1)
  Simulated 3D Taylor-Green Vortex (TGV)
    Can simulate transitional flow with reasonable dissipation rate
  mSPH similar to eddy viscosity model below numerical resolution
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 7: Large-Eddy Simulation-based Models
Implicit Pressure Poisson-based Models
  [Gotoh2004, 2005] Considered incompressible flow
  Filtered the Navier-Stokes (NS) eqs (Spatial filter)
  Stress Tensor  Closed using Boussinesq’s Hypothesis
  Eddy viscosity  Estimated using Smagorinsky Model
    Model is modified to incl wall effects, s.t., it is not over-dissipative inside laminar layer
  System evolved using the predictive-corrective time integrator
    Requires the implicit solution of the pressure poisson equation
  Simulated:
    2D wave interaction with partially immersed breakwater
    2D wave breaking on a beach
    Accurately tracked free surfaces with large deformation
    Surfaces did not exhibit numerical diffusion
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 8: Large-Eddy Simulation-based Models
Explicit Pressure Poisson-based Models
  [Rogers2005] Considered compressible flow
  Averaged the NS eqs (Favre averaging)
  Filtered the Navier-Stokes (NS) eqs (Spatial filter)
  Observed density variations in compressible SPH  Unphysical behaviour on free surfaces
    Performed Shepard filtering of density every 40 time steps
  Simulated:
    Weakly plunging breaker in 2D & 3D
    2D green-water overtopping, 2D & 3D wave breaking, 3D dam break [Rogers2006]
    Model predicted regions of high vorticity in 2D
    Model captured vertically oriented eddies in 3D
    Accurate for flow separation or splash-based problems
    Requires large number of particles, and very small time steps
    Uncertain regarding scalability to large-scale problems
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 9: Large-Eddy Simulation-based Models
Explicit Pressure Poisson-based Models
  [Canelas2016] Observed the standard Smagorinsky model cannot enforce wall conditions and non-vanishing stresses with laminar flows.
  Wall-adapting local eddy viscosity (WALE) model
  Simulated:
    Array of cylinders in 2D flow
    Studied LCS of the flow
    Observed recombination of vortices to larger structures
    Vortices with opposing strengths cancelled each other
    Believe such interactions lead to difficulty in interpreting the energy spectrum
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 10: Large-Eddy Simulation-based Models
Explicit Pressure Poisson-based Models
  [Okraschevski2022] Reinterpret SPH as a Lagrangian quadrature technique for explicit LES eqs
    Kernel scale limits SPH’s physical resolution  Unsuitable DNS alternative
  Considered spatial filtering on compressible NS
  Compared multiple Smagorinsky models (standard, sigma, MCG-form)
  Simulated 3D TGV
    All of the Smagorisnky models reduced the averaged kinetic energy
    Did not predict the dissipation rates accurately
  Overall comments:
    [fig2.14a,c]
    SPH can capture turbulence up to kernel scale at a high cost
    Explicit SFS models will remove kinetic energy, heightening the energy deficit of standard SPH
    Such models in an SPH framework can only degrade the quality of the approximation for subsonic turbulent flow [rennehan2021mixing]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 11: Lagrangian LES-based Models
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 12: RANS-based Models
[Shao2006, Wang2020]
  Considered incompressible, unsteady RANS equations
  Evolved using predictor-corrector scheme  Implicit pressure poisson equation
  Coefficients of the transport equations are empirically defined
  Simulated:
    2D wave breaking and overtopping of sloping wall [Shao2006]
    2D solitary wave propagating over a bottom-mounted barrier [Wang2020]
  Comments:
    coefficients derived from a quasi-steady state may behave sub-optimally in transient flow
    model would require further sensitivity analysis for the turbulence model and spatial resolution for improved results, despite being reasonably accurate in tracking free surfaces.
    Underpredicts max k, sensitive to initial seeding of k
    Effects of physical viscous dissipation and numerical dissipation needs to be balanced aptly
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 13: LANS-based Models
[holm1998euler, Marsden2001] Lagrangian averaged NS equations (LANS-) considered
  Averaging technique employed at the level of the variational principle from which NS eqs are derived
  denotes scale of rapid fluctuations in the flow map
[Monaghan2002] Formulated the SPH- model based on the LANS- eqs
  Considered smoothed velocity for particle transport
  Momentum eq had to solved iteratively
[Monaghan2011, Monaghan2017] Derived the SPH- model
  Explicit momentum equation with a viscous term
  Simulated 2D flow past a cylinder moving along a Lissajous curve
  predict satisfactory results for the velocity correlation functions, energy spectrum and mixing while having particle resolution be half of that required for a DNS with a resolution the Reynolds length
  higher Reynolds numbers and other boundary conditions, such as free surfaces, will need to be studied further
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 14: Miscellaneous Models
[Liu2019] Devised a viscosity-based vorticity correction technique
  Aimed primarily towards benefiting the CGI community
  Work focuses more on visual artifacts of the flow, not quantified metrics
  Builds on the fact that rotational kinetic energy translational kinetic energy
[Obeidat2018] Devised a hybrid-SPH scheme
  Employs Eulerian mesh to evaluate the governing equations
  Values interpolated to particles which advect
  Remeshing is performed when particle distribution is not uniform
  Information from the model cannot help improve traditional SPH schemes
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 15: Evaluation of Turbulence Models
Most of Lagrangian turbulent models seem to be tested for only complex surface flows
Systematic analysis of isotropic turbulence problems provides greater insight into the energy spectrum and its corresponding cascade across varying length scales.
Appropriate bounded/periodic test cases must be used when analyzing turbulence
Energy cascade might not always be apt? Use coherent structures, vorticity, other suitable metrics [Q]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 16: Benchmark Problems
Taylor-Green Vortex Problem
  2D Case
    Periodic, incompressible flow
    Analytical solutions known
  3D Case
    Initial flow conditions can be specified
Thin Double-Shear Layer
  Flow under-resolved  Spurious structures are produced
  Generation of the spurious structure depends on the scheme
3D Isotropic Turbulence
  DNS dataset from the JHU Turbulence database Cluster [li2008public]
  Dataset: Incompressible flow with isotropic and forced turbulence.
  - Spatial points, with time samples spanning one large-scale turnover time
2D Confined & Driven Turbulence
  2D fluid confined to a square box enclosing a cylinder
  Cylinder moves in a predetermined trajectory
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 17
Thank you!
Department of Aerospace Engineering
Indian Institute of Technology Bombay
October 25th, 2022

## Slide 18: Blank Template Slides

## Slide 19
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.

## Slide 21: Filled Template Slides

## Slide 22: Project Motivation
Motion of Biological Swimmers
Study of Forces
Study of Energetics
High-Fidelity - CFD Solvers
Simulation Parameters
Reynolds number
Swimming trajectories
Single/Multi Swimmers
Placements & Configurations
Boundary Conditions
Geometry
And many more...
Develop underwater vehicles with:
better mobility
lower noise
higher endurance
efficiency
Low-Fidelity - Theoretical or Computational Frameworks
Project Outcome
Gain better understanding of the problem at hand
Utilizes lesser resources
Allows for faster iteration over models

## Slide 23: Conclusion
Thrust produced continuously → Output is not stable.
Sharp peaks in thrust production coincide with vortex shedding.
Airfoil starts its heaving motion with downwards stroke → Small negative lift is produced (average)
Airfoil starts its heaving motion with upwards stroke → Small positive lift is produced (average).
General trend in bulk movement of shed vortices as shown by Dynnikova[1] is observed.
Fig: Vortex wakes behind an airfoil performing angular oscillations[7]
[1] Dynnikova, G. Ya et al. (2021). “Stability of a reverse Karman vortex street”. In: Physics of Fluids 33.2. ISSN: 10897666. DOI: 10.1063/5.0035575.