## Slide 1: Turbulence Modelling for Smoothed Particle Hydrodynamics K T Prajwal Prathiksh
Supervisor: Prof. Prabhu Ramachandran
Department of Aerospace Engineering
Indian Institute of Technology Bombay
June 30th, 2023
Dual Degree Project (Stage II) - Presentation

## Slide 2: Introduction
Lagrangian Modelling – SPH
  No background mesh
  Handles large deformations, complex boundary dynamics
  Simplified model implementation
  Highly & efficiently parallelizable
Turbulent Flow
  Characterization
      High Reynolds number flows
      Random spatial & temporal velocity fluctuations
      Rotational & 3D velocity field
      Large mixing capacity of the flow
      Chaotic nature of solutions
  Modelling
      Lacks analytical solutions except for simple cases
      CFD simulations required for complex flows
      Typical modelling techniques
          Governing equations  Averaged or filtered
          Closure problem  Fluctuating components modelled using mean flow properties
          Stochastic methods
      Models mostly based on Eulerian framework

## Slide 3: Project Objectives
Turbulence Modelling in SPH
  Lacks robust & accurate models
  Shortcomings of current models
    Cannot be generalized to various types of turbulence-based problems
    Issues in scaling to 3D turbulent flows
      Accuracy & computational constraints
    Boundary conditions & treatment not well established
Project Objective
  Review state of the art turbulence models in SPH
  Document advantages & disadvantages of the major categories of models
  Identify representative schemes from each category
  Analyze & study their performance for high Reynolds number (Re) flows
  Attempt at improving their accuracy & robustness using recent developments in SPH
Existing
Models
Expected
Outcome

## Slide 4: Post-Simulation Analysis
Energy spectral density
  Velocity field over a grid generated using suitable interpolation of the particle velocity data[1]
  Fourier transform of the velocity field  Velocity spectrum as a function of the wave-number
  Energy spectrum computed from the velocity spectrum
Velocity gradient-based metrics
  Iso-vorticity surfaces, Q-criterion, -criterion, etc.
  Most of the definitions for a vortex  Not objective & suitable for studying the flow (esp. 3D flow)[2]
Lagrangian coherent structures (LCS)
  Local velocity fluctuations do not induce noise in LCS
  FTLE is formulated in the Lagrangian framework  Better identification of LCSs
  Provides flexibility in its formulation[3]
    Backward-in-time FTLE can be computed using limited resources during run-time concurrently
    Forward-in-time FTLE can only be computed during post-processing
    Easily parallelizable
[1] Y. Shi, X. X. Zhu, M. Ellero, and N. A. Adams, “Analysis of interpolation schemes for the accurate estimation of energy spectrum in Lagrangian methods,” Comput. Fluids, vol. 82, pp. 122–131, 2013, doi: 10.1016/j.compfluid.2013.05.003.
[2] G. Haller, “An objective definition of a vortex,” J. Fluid Mech., vol. 525, pp. 1–26, 2005.
[3] P. N. Sun, A. Colagrossi, S. Marrone, and A. M. Zhang, “Detection of Lagrangian Coherent Structures in the SPH framework,” Comput. Methods Appl. Mech. Eng., vol. 305, pp. 849–868, 2016, doi: 10.1016/j.cma.2016.03.027.
Notes: Vortices are often thought of as regions of high vorticity, but there is no universal threshold over which vorticity is to be considered high. Definitions requiring closed or spiralling streamlines for a vortex are also ambiguous, because streamline topology changes even under simple Galilean transformations such as constant speed translations

## Slide 5: Energy Spectral Analysis
Implementation
  Interpolated vel. Field  Fourier Transform (numpy.fft.fftn)
  : Integrating over sphere, between limits
Test Case: Expected decay rate
Observations:
  Computation without interpolation  ‘Best’-case
  Interpolation  Energy captured at higher is reduced
  ‘Low-pass’ filter behaviour
    Fig: Scalar for 2D case with

## Slide 6: Energy Spectral Analysis
    Fig: Scalar for 2D case for various perturbation amplitudes
    Fig: Scalar for 2D case for various interpolation methods
    Fig: Scalar for 2D case for various kernels
Observations
  Disorder in particle spacing: Counters effect of reduced energy in higher
  Interpolation method: sph counters effect of reduced energy the most
  Kernels: WendlandQuincticC6 counters effect of reduced energy the most
  Resolution: Improves accuracy throughout
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 7: Finite-time Lyapunov Exponent (FTLE) Field Analysis
Implementation
  Work of Sun, Colagrossi et al. 2016
  Define Function of of particles at two time-instances
  Calculate Cauchy-Green tensor field
  Calculate max./min. eigenvalue of the tensor field
Test-Case: Spiral displacement field
Observations
  Current implementation  Qualitative results only
  Not as accurate either
  Consider implementation of tracer particles, or in situ FTLE computation for improved capturing of LCSs
    Fig: Spiral displacement field
    Vid: FIT - FTLE. (Rep: Brunton 2022)
[1] P. N. Sun, A. Colagrossi, S. Marrone, and A. M. Zhang, “Detection of Lagrangian Coherent Structures in the SPH framework,” Comput. Methods Appl. Mech. Eng., vol. 305, pp. 849–868, 2016, doi: 10.1016/j.cma.2016.03.027.
[2] S. L. Brunton (2022, February 11), Lagrangian Coherent Structures (LCS) in unsteady fluids with Finite Time Lyapunov Exponents (FTLE)

## Slide 8: Turbulence Models
Surveyed research papers detailing work on turbulence models for SPH (c. 2000 – 2022)
Classified 5 major categories of turbulence models
Identified the following representative schemes
Devised a systematic, model-evaluation method to quantify order of convergence (OOC)
  Identify OOC using TGV problem
  Post-simulation analysis techniques: error; energy-spectrum; velocity field
Turbulence Model | Scheme Name | Reference
Viscosity – based (Standard Lagrangian) | Lagrangian with iterative PST and coupled_c viscosity formulation (L-IPST-C) | Negi et al. 2022
LES – based (Explicit P-EOS) | SPH-LES | Okraschevski et al. 2022
Lagrangian-LES – based | -LES-SPH | Antuono et al. 2021
RANS – based | SPH | Songdong Shao 2006
LANS - based | SPH- | J. J. Monaghan 2017
Turbulence Model | Scheme Name | Reference
Viscosity – based (Standard Lagrangian) | Lagrangian with iterative PST and coupled_c viscosity formulation (L-IPST-C) | Negi et al. 2022
LES – based (Explicit P-EOS) | SPH-LES | Okraschevski et al. 2022
Lagrangian-LES – based |  | Antuono et al. 2021
RANS – based |  | Songdong Shao 2006
LANS - based |  | J. J. Monaghan 2017
    Tab: Representative turbulent SPH schemes
Turbulence Models
Viscosity
LES
Lagrangian-LES
RANS
LANS
Artificial
Stochastic
Implicit P-Poisson
Explicit P-EOS
Standard Lagrangian
    Fig: Chart of the major categories of turbulence models in SPH

## Slide 9: Viscosity-based Model (L-IPST-C)
Standard Lagrangian Formulation
  No artificial viscosity added to the MOM eq.
  implemented using coupled_c formulation
  Iterative particle shifting technique employed
    Redistributes particles
    Particle properties updated through Taylor-series exp.
  Simulated multiple problems: TGV, Gresho vortex, & Kelvin-Helmholtz
  Used RK2 integrator
  Comments
    Identified SPH approximation of operators to achieve second-order convergence (SOC)
    Identified the optimum kernel and kernel radius for SOC
    Recommended to use density as a fluid property instead of summation density
    Recommended scheme observed to be SOC for a wide variety of problems
[1] P. Negi and P. Ramachandran, “Techniques for second-order convergent weakly compressible smoothed particle hydrodynamics schemes without boundaries,” Phys. Fluids, vol. 34, no. 8, p. 087125, 2022, doi: 10.1063/5.0098352.
    Fig: Convergence rates for pressure (left) and velocity (right) of different variants of SOC schemes. (Rep: Negi2022)

## Slide 10: Viscosity-based Model (L-IPST-C) Analysis
    Fig: Convergence of the L-IPST-C scheme for various time-integrators
    Fig: Convergence of the L-IPST-C scheme for various time-integrators
    Fig: Run-time (in s) of the L-IPST-C scheme for various time-integrators
Observations
  Order of integrator: Negligible on SOC & magnitude of error
  More important factors for SOC
  increases: Scheme loses SOC
  Run-times: PEC integrator faster than the slowest, while maintaining accuracy & SOC
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 11: Large-Eddy Simulation-based Model (SPH-LES)
Explicit Pressure EOS-based Models[1]
  Reinterpret SPH  Lagrangian quadrature technique for explicit LES
    Kernel scale limits SPH’s physical resolution  Unsuitable DNS alternative
  Navier-Stokes (NS) eqs.  Spatially filtered
  Compared multiple Smagorinsky models
    (standard, , MCG-form)
  Simulated 3D TGV
  Comments
    Smagorisnky models reduced averaged kinetic energy
    Dissipation rates not predicted accurately
    SPH can capture turbulence up to kernel scale (high cost)
    Explicit SGS models remove kinetic energy  Increases energy deficit of standard SPH
    “SGS models in SPH framework only degrade the quality of the subsonic turbulent flow approximation”[2]
[1] M. Okraschevski, N. Bürkle, R. Koch, and H.-J. Bauer, “Smoothed Particle Hydrodynamics Physically Reconsidered -- The Relation to Explicit Large Eddy Simulation and the Issue of Particle Duality,” 2022, [Online].
[2] D. Rennehan, “Mixing matters,” Mon. Not. R. Astron. Soc., vol. 506, no. 2, pp. 2836–2852, 2021.
Fig: Density-weighted averaged kinetic energy (top), averaged dissipation rate (bottom). (Rep: Okraschevski et al)

## Slide 12: Large-Eddy Simulation-based Model (SPH-LES) Analysis
    Fig: Convergence of the SPH-LES scheme for various values
    Fig: Velocity magnitude field for SPH-LES scheme
    Fig: Velocity magnitude field for SPH-LES scheme
Observations
  :
    No effect on the SOC or accuracy of the scheme
    No PST  Clustering of particles; Domain is no longer uniform
  : No effect on the SOC or accuracy
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 13: Lagrangian LES-based Model (-LES-SPH)
Lagrangian form of LES[1,2]
  Assumption: Weakly compressible flow
  Lagrangian filter - (compact support, even) introduced
  decomposed into independent spatial & temporal components
  Governing eqs. written using spatially filtered terms
    Temporal terms of higher order neglected
    Continuity eq. closed using Fick-like diffusion term
    MOM eq. closed using Yoshizawa-model for the stress tensor
    Considered -SPH formulation
  Simulated:
    2D TGV
    3D homogenous turbulence
  Comments
    The model overcomes issues of spurious high-frequency noise & onset of tensile instability (High flows)
    The energy spectra agrees well with theoretical decay rate
    Wall functions need to be incorporated to deal with boundaries
    Higher-order approach can significantly improve the performance
[1] A. Di Mascio, M. Antuono, A. Colagrossi, and S. Marrone, “Smoothed particle hydrodynamics method from a large eddy simulation perspective,” Phys. Fluids, vol. 29, no. 3, 2017, doi: 10.1063/1.4978274.
[2] A. Colagrossi, “Smoothed particle hydrodynamics method from a large eddy simulation perspective . Generalization to a quasi-Lagrangian model Smoothed particle hydrodynamics method from a large eddy simulation perspective . Generalization to a quasi-Lagrangian model,” vol. 015102, no. December 2020, 2021, doi: 10.1063/5.0034568.
Fig: Energy spectrum (left), field (right). (Rep: Colagrossi2021)

## Slide 14: Lagrangian LES-based Model (-LES-SPH) Analysis
    Fig: Convergence of the -LES-SPH () scheme for various equations of state
    Fig: Convergence of the -LES-SPH () scheme various values
    Fig: Convergence of the -LES-SPH () scheme various time integrators
Observations
  -LES-SPH (): Offers better OOC when used with TaitEOS than the other combinations
  :
    Magnitude of error is least when PST is disabled
    OOC improves with PST as well as the nature of the velocity field
  Integrator: RK2 offers the best OOC and is faster
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 15: RANS-based Model (SPH)
Models[1,2]
  Considered incompressible, unsteady RANS equations
  Predictive-corrective time integrator
    Requires implicit solution of pressure poisson eq
  Simulated:
    2D wave breaking and overtopping of sloping wall[1]
    2D solitary wave propagating over a bottom-mounted barrier[2]
  Comments
    Accurately tracks free-surfaces
    coefficients (empirically derived from quasi-steady state) perform sub-optimally in transient flow
    Model requires a sensitivity analysis for the turbulence model & spatial resolution for improved performance
    Underpredicts max & is sensitive to initial seeding of
    Effects of viscous dissipation & numerical dissipation need to be balanced
[1] S. Shao, “Incompressible SPH simulation of wave breaking and overtopping with turbulence modelling,” no. May 2005, pp. 597–621, 2006.
[2] D. Wang and P. L. F. Liu, “An ISPH with k–ε closure for simulating turbulence under solitary waves,” Coast. Eng., vol. 157, no. July 2019, p. 103657, 2020, doi: 10.1016/j.coastaleng.2020.103657.
Fig: Water surface elevations. (Rep: Shao et al)c

## Slide 16: RANS-based Model (SPH) Analysis
    Fig: Convergence of the spatial operators - transport equation (Test-case: 1)
    Fig: Convergence of the spatial operators - transport equation (Test-case: 2)
    Fig: Convergence of the SPH scheme for various equations of state
Observations
  SPH discretisation:
    Variant with simplified transport equations is SOC
    Increased speed of sound  Improved accuracy
  EOS:
    Negligible effect on SOC & accuracy
    TaitEOS better captures the velocity field
  :
    No effect on the SOC or accuracy of the scheme
    No PST  Clustering of particles; Domain is no longer uniform
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 17: LANS-based Model (SPH-)
Lagrangian-averaged NS eqs. (LANS-) Models[1,2,3,4]
  Lagrangian-averaging[1]: Performed at the level of variational principle from which NS eqs. are derived
    denotes scale of rapid fluctuations in the flow map
  SPH- model[2]  Initial models based on LANS- eqs.
    Particle transport  Smoothed velocity
    MOM eq. solved iteratively
  SPH- model[3,4]  Improvement of SPH- model
    Explicit MOM eq. with viscous term
  Simulated 2D flow past a cylinder moving along a Lissajous curve[4]
  Comments
    Bounded (no-slip) flow implies is neither periodic/isotropic  Author prefers correlation functions over energy spectrum
    Satisfactory results for velocity correlation functions, energy spectrum & mixing with half the particle resolution of DNS
    Flows with larger Reynolds numbers & other boundary conditions, such as free surfaces need to be studied
[1] J. E. Marsden and S. Shkoller, “Global well-posedness for the Lagrangian averaged Navier-Stokes (LANS-α) equations on bounded domains,” Philos. Trans. R. Soc. A Math. Phys. Eng. Sci., vol. 359, no. 1784, pp. 1449–1468, 2001, doi: 10.1098/rsta.2001.0852.
[2] J. J. Monaghan, “SPH compressible turbulence,” vol. 852, pp. 843–852, Apr. 2002, doi: 10.1046/j.1365-8711.2002.05678.x.
[3] J. J. Monaghan, “A turbulence model for smoothed particle hydrodynamics,” Eur. J. Mech. B/Fluids, vol. 30, no. 4, pp. 360–370, 2011, doi: 10.1016/j.euromechflu.2011.04.002.
[4] J. J. Monaghan, “SPH-ϵ simulation of 2D turbulence driven by a moving cylinder,” Eur. J. Mech. B/Fluids, vol. 65, pp. 486–493, 2017, doi: 10.1016/j.euromechflu.2017.03.011.
Fig: Stirring of coloured particles. (Rep: Monaghan2017)

## Slide 18: LANS-based Model (SPH-) Analysis
    Fig: Convergence of the SPH- scheme without and with gradient correction
    Fig: Convergence of the SPH- scheme for various values of
    Fig: Convergence of the SPH- scheme for various equations of state
Observations
  Gradient correction: No effect on the SOC, accuracy, velocity field or energy spectrum of the scheme
  : No effect on the SOC or accuracy of the scheme; Increased  More diffused velocity field
  EOS: No effect on the SOC, accuracy, velocity field or energy spectrum of the scheme
  :
    Larger values  Reduced magnitude of error but no apparent effect on SOC
    Larger values/No PST  Clustering of particles; Domain is no longer uniform
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 19: Long-time Simulation - Taylor-Green Vortex Problem
Turbulence Model | Scheme Name | PST Frequency | Equation of State | Integrator | CFL | Scheme-specific Parameters | Time Taken (s)
Viscosity – based (Standard Lagrangian) | Lagrangian with iterative PST and coupled_c viscosity formulation (L-IPST-C) | 10 | TaitEOS | PEC | 1 | --- | 5900
LES – based (Explicit P-EOS) | SPH-LES | 10 | TaitEOS | PEC | 1 | Viscous models=[SMAG, SMAG-MCG, SIGMA]; | ---
Lagrangian-LES – based | -LES-SPH | 10 | TaitEOS | RK2 | 1.5 | No gradient correction; | 8200
RANS – based | SPH | 10 | TaitEOS | PEC | 1 | Simplified transport equations; | 6400
LANS - based | SPH- | 10 | TaitEOS | PEC | 1 | No gradient correction; =0.5; | 3000
Turbulence Model | Scheme Name | PST Frequency | Equation of State | Integrator | CFL | Scheme-specific Parameters | 
Viscosity – based (Standard Lagrangian) | Lagrangian with iterative PST and coupled_c viscosity formulation (L-IPST-C) | 10 | TaitEOS | PEC | 1 | --- | 5900
LES – based (Explicit P-EOS) | SPH-LES | 10 | TaitEOS | PEC | 1 | Viscous models=[SMAG, SMAG-MCG, SIGMA]; | ---
Lagrangian-LES – based |  | 10 | TaitEOS | RK2 | 1.5 | No gradient correction; | 8200
RANS – based |  | 10 | TaitEOS | PEC | 1 |  | 6400
LANS - based |  | 10 | TaitEOS | PEC | 1 |  | 3000
Optimised SPH schemes documented
Long-time test-case
  TGV problem
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 20: Long-time Simulation Analysis
    Fig: Evolution of the angular momentum for various schemes (zoomed in)
    Fig: Evolution of the linear momentum for various schemes (zoomed in)
    Fig: Evolution of the linear momentum for various schemes
Observations
  No external forces  Angular & linear momentum should be conserved
  L-IPST-C & -LES-SPH :
    Oscillate about zero
    Stay bounded; Increased resolution  bounds decrease
  SPH : Almost perfectly conservative
  SPH- :
    Arbitrary jumps in the momentum plots  Not conservative
    Increased resolution  No convergence
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 21: Long-time Simulation Analysis
    Fig: Evolution of the kinetic energy for various schemes
    Fig: Evolution of the kinetic energy for various schemes (zoomed in)
    Fig: Evolution of the velocity decay for various schemes (zoomed in)
Observations
  L-IPST-C & -LES-SPH :
    Track exact solution accurately
    Increased resolution  Increased accuracy
  SPH : Dissipates all the energy  Non-physical solution
  SPH- : Adds energy to the system  System diverges
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 22: Long-time Simulation Analysis
    Fig: Evolution of the error for various schemes
    Fig: Velocity magnitude field (arrows represent the velocity vector) for various schemes
    Fig: Vorticity magnitude field (arrows represent the velocity vector) for various schemes
Observations
  L-IPST-C & -LES-SPH :
    Have relatively the least amount of error
    Capture both the velocity and vorticity field accurately
  SPH : Drains all the energy from the system; No structure in the flow field
  SPH- :
    High magnitude of error
    TGV structures present in the flow field, albeit with the magnitude blown-up
    Addition of a dissipative mechanism  Might improve performance
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 23: Long-time Simulation Analysis
    Fig: Evolution of the error (pressure) for various schemes
    Fig: Pressure magnitude field (arrows represent the velocity vector) for various schemes
    Fig: Density magnitude field (arrows represent the velocity vector) for various schemes
Observations
  L-IPST-C: Least amount of error; Reduces with resolution
  -LES-SPH:
    Significantly dependent on the resolution
    Trends in density & pressure field are captured well, but the limits are larger
  SPH : Non-existent and noisy density & pressure fields
  SPH- :
    Comparable error to -LES-SPH, and similar (but exaggerated) cause as well
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 24: Long-time Simulation Analysis
    Fig: Evolution of the energy spectrum (L-IPST-C)
    Fig: Evolution of the energy spectrum (-LES-SPH)
    Fig: Evolution of the energy spectrum (SPH-)
Observations
  L-IPST-C & -LES-SPH :
    Similar energy dissipation over time
    -LES-SPH  slightly better at redistributing energy to smaller scales
  SPH : Dissipates energy at all scales
  SPH- : Increases energy to the smaller scales; negligible effect on larger scales
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 25: Conclusion & Future Work
Stage – I outcome:
  A reasonable compilation of past SPH turbulence models
  The corresponding advantages, limitations & potential areas for refinement are understood
Entropically Damped Artificial Compressibility (EDAC) scheme[1]  Explicit incompressible SPH method
  Uses a pressure evolution eq. instead of the continuity equation[2]
  Produces a smoother & accurate pressure distribution for flows, confined or free
  Does not require artificial viscosity
Turbulence Models for EDAC
  Incompatible with RANS due to incompressibility condition
    Will consider compressible EDAC scheme to devise a turbulence model
  Lagrangian LES filtering of the pressure eq  Mixed filtered term obtained; cannot be decoupled further
    Will investigate potential closure models to decouple/model the mixed term
[1] P. Ramachandran and K. Puri, “Entropically damped artificial compressibility for SPH,” Comput. Fluids, vol. 179, pp. 579–594, Jan. 2019, doi: 10.1016/j.compfluid.2018.11.023.
[2] J. R. Clausen, “Entropically damped form of artificial compressibility for explicit simulation of incompressible flow,” Phys. Rev. E - Stat. Nonlinear, Soft Matter Phys., vol. 87, no. 1, pp. 1–12, 2013, doi: 10.1103/PhysRevE.87.013309.

## Slide 26
Acknowledgements
I would like to acknowledge the mentorship of my guide, Prof. Prabhu Ramachandran, and the members of his lab group for their inputs and support.
I also appreciate the research environment provided by the Indian Institute of Technology Bombay, and particularly, the Department of Aerospace Engineering for having given me this platform to pursue my graduate studies.
I am also thankful for the professors on the panel for their time today, and allowing me to present my work.
Department of Aerospace Engineering
Indian Institute of Technology Bombay
June 30th, 2023
Thank you!

## Slide 27: Appendix A -- Additional Results --

## Slide 28: Large-Eddy Simulation-based Model (SPH-LES) Analysis
    Fig: Convergence of the SPH-LES scheme for various speed of sound values
    Fig: Velocity magnitude field for SPH-LES scheme
    Fig: Velocity magnitude field for SPH-LES scheme
Observations
  : No effect on the SOC or accuracy
  Negligible difference in the distribution of the particles
  chosen, based on run-time and accuracy trade-off
  Go back
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 29: Lagrangian LES-based Model (-LES-SPH) Analysis
    Fig: Convergence of the -LES-SPH () scheme for various equations of state
    Fig: Velocity magnitude field for -LES-SPH () scheme
    Fig: Velocity magnitude field for -LES-SPH () scheme
Observations
  -LES-SPH (): Offers better OOC when used with TaitEOS than the other combinations
  : Magnitude of error is least when PST is disabled; but OOC improves with PST
  Go back
TaitEOS
LinearEOS
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 30: RANS-based Model (SPH) Analysis
    Fig: RHS of -transport equation (Test-case: 1) (Simplified eqns.)
    Fig: RHS of -transport equation (Test-case: 1) (Expanded eqns.)
    Fig: Convergence of the spatial operators - transport equation (Test-case: 2)
Simplified eqns.
Expanded eqns.
Go back
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 31: RANS-based Model (SPH) Analysis
    Fig: Velocity magnitude field for SPH scheme (LinearEOS)
    Fig: Velocity magnitude field for SPH scheme (TaitEOS)
    Fig: Velocity magnitude field for SPH scheme
Observations
  SPH discretisation:
    Variant with simplified transport equations is SOC
    Increased speed of sound  Improved accuracy
  EOS:
    Negligible effect on SOC & accuracy
    TaitEOS better captures the velocity field
  :
    No effect on the SOC or accuracy of the scheme
    No PST  Clustering of particles; Domain is no longer uniform
  Go back
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 32: LANS-based Model (SPH-) Analysis
    Fig: Velocity magnitude field for SPH- scheme
    Fig: Velocity magnitude field for SPH- scheme
    Fig: Convergence of the SPH- scheme for various values
Observations
  Gradient correction: No effect on the SOC, accuracy, velocity field or energy spectrum of the scheme
  : No effect on the SOC or accuracy of the scheme; Increased  More diffused velocity field
  EOS: No effect on the SOC, accuracy, velocity field or energy spectrum of the scheme
  :
    Larger values  Reduced magnitude of error but no apparent effect on SOC
    Larger values/No PST  Clustering of particles; Domain is no longer uniform
  Go back
Notes: http://people.atmos.ucla.edu/jcm/turbulence_course_notes/2D_homogeneous.pdf
Equilibrium Inertial Cascade Ranges

## Slide 33: Appendix B -- Additional Turbulence SPH Models --

## Slide 34: Viscosity-based Models
Eddy Viscosity Model[1]
  One of the first classes of SPH turbulence models
  Velocities are Reynolds-averaged
  First-order closure model:
    Reynolds stress tensor & mean velocity gradients
  Turbulent eddy viscosity considered
  Simulated Poiseuille flow
  Comments
    Reproduced log-law profile near walls
    Appropriate for shear flows
[1] D. VIOLEAU, S. PICCON, and J.-P. CHABARD, “TWO ATTEMPTS OF TURBULENCE MODELLING IN SMOOTHED PARTICLE HYDRODYNAMICS,” in Advances in Fluid Modeling and Turbulence Measurements, Jul. 2002, vol. 1, no. 5, pp. 339–346, doi: 10.1142/9789812777591_0041.
Fig: Computed mean velocity profile of turbulent Poiseuille flow in a pipe (Rep: Violeau et al)

## Slide 35: Viscosity-based Models
Generalized Langevin Model[1]
  Prescribed the particle velocity as a random process
  Acceleration  Function of a random vector (non-correlated with velocity)
  Simulated Poiseuille flow
  Comments
    Mean operator appeared to behave like a LES filter
    Large deviations observed in mean velocity profile
    Can be generalized to various types of turbulent flows, & not only shear flows
[1] D. VIOLEAU, S. PICCON, and J.-P. CHABARD, “TWO ATTEMPTS OF TURBULENCE MODELLING IN SMOOTHED PARTICLE HYDRODYNAMICS,” in Advances in Fluid Modeling and Turbulence Measurements, Jul. 2002, vol. 1, no. 5, pp. 339–346, doi: 10.1142/9789812777591_0041.
Fig: Computed mean velocity profile of turbulent Poiseuille flow in a pipe (Rep: Violeau et al)

## Slide 36: Viscosity-based Models
Modified-SPH (mSPH)[1]
  Observation: Absence of viscosity  Noisy particle motion
  Finite viscosity  Over-prediction of dissipation
  Modified EOS & MOM eqs.  Particle distribution homogenised
  Simulated:
    2D Taylor-Green Vortex (TGV)
    3D Taylor-Green Vortex (TGV)
  Comments
    Merging of vortices observed
    Energy cascade (Kolmogorv scale) slopes reproduced
      mSPH (-3); standard SPH (1)
    Transitional flow simulated with reasonable dissipation rate
    mSPH Eddy viscosity model below numerical resolution
[1] S. Adami, X. Y. Hu, and N. A. Adams, “Simulating three-dimensional turbulence with SPH,” 2012.
Fig: Velocity vector plot at t=2 (left) and t=30 (right). (Rep: Adami et al)

## Slide 37: Large-Eddy Simulation-based Models
Implicit Pressure Poisson-based Models[1,2]
  Assumption: Incompressible flow
  Navier-Stokes (NS) eqs.  Spatially filtered
  Stress tensor  Closed using Boussinesq’s hypothesis
  Eddy viscosity  Estimated using modified Smagorinsky model
    Model modified to include wall effects
  Predictive-corrective time integrator
    Requires implicit solution of pressure poisson eq
  Simulated:
    2D wave interaction with partially immersed breakwater[1]
    2D wave breaking on a beach[2]
  Comments
    Accurately tracked free surfaces with large deformation
    Surfaces did not exhibit numerical diffusion
    Scheme’s accuracy:
[1] H. Gotoh, S. Shao, and T. Memita, “SPH-LES model for numerical investigation of wave interaction with partially immersed breakwater,” Coast. Eng. J., vol. 46, no. 1, pp. 39–63, 2004, doi: 10.1142/S0578563404000872.
[2] S. Shao and H. Gotoh, “Turbulence particle models for tracking free surfaces,” J. Hydraul. Res., vol. 43, no. 3, pp. 276–289, May 2005, doi: 10.1080/00221680509500122.
Fig: Time sequences of wave profile. (Rep: Gotoh et al)
Notes: Model is modified to include wall effects, s.t., it is not over-dissipative inside laminar layer

## Slide 38: Large-Eddy Simulation-based Models
Explicit Pressure EOS-based Models[1,2]
  Assumption: Compressible flow
  NS eqs  Favre averaged
  Observation: Density variations  Unphysical behaviour on free surfaces
    Shepard filtering of density performed periodically
  Simulated:
    Weakly plunging breaker in 2D & 3D[1]
    2D green-water overtopping, 2D & 3D wave breaking, 3D dam break[2]
  Comments
    Model predicted regions of high vorticity in 2D
    Model captured vertically oriented eddies in 3D
    Accurate for flow separation or splash-based problems
    Requires large & very small
    Uncertain regarding scalability to large-scale problems
[1] B. D. ROGERS and R. A. DALRYMPLE, “SPH MODELING OF BREAKING WAVES,” in Coastal Engineering 2004, Apr. 2005, pp. 415–427, doi: 10.1142/9789812701916_0032.
[2] R. A. Dalrymple and B. D. Rogers, “Numerical modeling of water waves with the SPH method,” vol. 53, pp. 141–147, 2006, doi: 10.1016/j.coastaleng.2005.10.004.

## Slide 39: Large-Eddy Simulation-based Models
Explicit Pressure EOS-based Models[1]
  Observation: Standard Smagorinsky model cannot enforce
    Wall conditions
    Non-vanishing stresses with laminar flows
  Devised Wall-adapting local eddy viscosity model (WALE)
  Simulated an array of cylinders in 2D flow
  Comments
    LCS captured reasonably well
    Observed merging of vortices to larger structures
    Interactions of vortices with opposing strengths  Vorticity cancellation
    Claim: Complex vortex interactions  Possible difficulty in interpreting the energy spectrum
[1] R. B. Canelas, A. M. Ricardo, R. M. L. Ferreira, J. M. Domínguez, and A. J. C. Crespo, “Hunting for Lagrangian Coherent Structures : SPH-LES turbulence simulations with Wall-adapting Local Eddy Viscosity ( WALE ) model,” 11th SPHERIC, no. March 2017, 2016, [Online].
Fig: Backward-in-time FTLE field. (Rep: Canelas et al)

## Slide 40: Miscellaneous Models
Viscosity-based vorticity correction model[1]
  Aimed primarily towards benefiting the CGI community
    Faster computational time & simplified system of equations
  Research focuses more on visual artifacts of the flow, not quantified metrics
  Builds on the fact that rotational kinetic energy translational kinetic energy
Hybrid-SPH (hrSPH)[2]
  Particle data interpolated onto Eulerian mesh grids
  Rate of change of flow properties computed on mesh grid
  Updated mesh values interpolated onto particles
  Advection of particles using the updated properties
  Remeshing is performed when particles cluster to ensure uniform particle distribution
  Information from the model cannot help improve traditional SPH schemes
[1] S. Liu, X. Wang, X. Ban, Y. Xu, J. Zhou, and Y. Zhang, “Viscosity-based Vorticity Correction for Turbulent SPH Fluids,” in 2019 IEEE Conference on Virtual Reality and 3D User Interfaces (VR), Mar. 2019, pp. 1048–1049, doi: 10.1109/VR.2019.8798224.
[2] A. Obeidat and S. P. A. Bordas, “Three-dimensional remeshed smoothed particle hydrodynamics for the simulation of isotropic turbulence,” Int. J. Numer. Methods Fluids, vol. 86, no. 1, pp. 1–19, 2018, doi: 10.1002/fld.4405.

## Slide 41
Evaluation of Turbulence Models
Most of Lagrangian turbulent models  Tested for primarily complex, free-surface flows
A systematic analysis of isotropic turbulence problems provides better insight on the energy spectrum & its cascade across varying length scales
Appropriate bounded/periodic test cases must be used when analyzing turbulence
Analyse results with appropriate metrics, and validate the results with experimental or numerical data from literature
Benchmark Problems
Various Turbulence Models
Post-simulation Analysis
Model Validation
Model Improvement

## Slide 42: Benchmark Problems
Taylor-Green Vortex Problem  Periodic, incompressible flow
  2D Case: Analytical solutions known
  3D Case: Initial flow conditions can be specified
Thin Double-Shear Layer
  Flow under-resolved  Spurious structures are produced
  Generation of the spurious structure depends on the scheme
3D Isotropic Turbulence[1]
  DNS dataset from the JHU Turbulence database Cluster
  Dataset: Incompressible flow with isotropic and forced turbulence.
  spatial points & time samples spanning one large-scale turnover time
2D Confined & Driven Turbulence[2]
  2D fluid confined to a square box enclosing a cylinder
  Cylinder moves in a predetermined trajectory
[1] Y. Li et al., “A public turbulence database cluster and applications to study Lagrangian evolution of velocity increments in turbulence,” J. turbul., vol. 9, p. N31, 2008.
[2] J. J. Monaghan, “SPH-ϵ simulation of 2D turbulence driven by a moving cylinder,” Eur. J. Mech. B/Fluids, vol. 65, pp. 486–493, 2017, doi: 10.1016/j.euromechflu.2017.03.011.